Workpaper PGECOHVC123

94 AFUE Furnace - Res

Revision # 2

Pacific Gas & Electric Company

Customer Energy Efficiency Department

94 AFUE Central Natural Gas Furnace - Residential

Measure Codes: H731, H732

# At-A-Glance Summary

| Applicable Measure Codes: | H731 and H732 |
| --- | --- |
| Measure Description: | This measure applies to the installation of a 94% AFUE efficiency central natural gas furnace with and without variable speed motor in a residential dwelling. |
| Energy Impact Common Units: | kW, kWh, and Therms Per household |
| Base Case Description: | Source: Title 20 Gas furnace meeting T20 base case requirements of 78% AFUE. |
| Base Case Energy Consumption: | Source: DEER 2008. Depends on climate zone, dwelling type, and vintage. |
| Measure Energy Consumption: | Source: DEER 2008. Depends on climate zone, dwelling type, and vintage. |
| Energy Savings (Base Case – Measure) | Source: DEER 2008. Depends on climate zone, dwelling type, and vintage. |
| Costs Common Units: | $ Per furnace. |
| Base Case Equipment Cost ($/unit): | Source: DEER 2008. Varies, see At-A-Glance Measure List |
| Measure Equipment Cost ($/unit): | Source: DEER 2008. Varies, see At-A-Glance Measure List |
| Measure Incremental Cost ($/unit): | Source: DEER 2008. Varies, see At-A-Glance Measure List |
| Effective Useful Life (years): | Source: DEER 2008. 20 years for furnace only 15 years for furnace with variable speed motor (VSM) |
| Program Type: | Retrofit and Replace on Burnout |
| Net-to-Gross Ratios: | Source: DEER 2008. 0.60, NTGR Values for Residential Measures spreadsheet |
| Important Comments: |  |

At-A-Glance Measure List

| Measure Code | DEER Impact ID | Measure Description | Building Type | Building Vintage | Climate Zone | Peak Electric Demand Reduction (kW/household) | Electric Savings (kWh/household) | Gas Savings (therms/ household) | Base Case Cost ($/household) | Measure Cost ($/household) | Measure Incremental Cost ($/household) | Effective Useful Life (years) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | OTR | AV | OTR | 0 | 0 | 0.00 | $0.00 | $0.00 | $0.00 |  |
| H731 | DMO-w01-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | DMO | AV | Z01 | 0 | 0 | 53.89 | $476.55 | $1,322.89 | $524.98 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | MFM | AV | Z01 | 0 | 0 | 22.93 | $344.69 | $879.63 | $302.50 | 20 |
| H731 | SFM-w01-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | SFM | AV | Z01 | 0 | 0 | 48.46 | $344.69 | $1,393.19 | $680.35 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | OTR | AV | Z01 | 0 | 0 | 22.93 | $344.69 | $879.63 | $302.50 | 20 |
| H731 | DMO-w02-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | DMO | AV | Z02 | 0 | 0 | 51.77 | $476.97 | $1,324.06 | $525.44 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | MFM | AV | Z02 | 0 | 0 | 23.38 | $545.93 | $1,393.19 | $479.11 | 20 |
| H731 | SFM-w02-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | SFM | AV | Z02 | 0 | 0 | 49.43 | $545.93 | $1,203.82 | $339.78 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | OTR | AV | Z02 | 0 | 0 | 23.38 | $545.93 | $1,393.19 | $479.11 | 20 |
| H731 | DMO-w03-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | DMO | AV | Z03 | 0 | 0 | 46.42 | $476.78 | $1,323.54 | $525.23 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | MFM | AV | Z03 | 0 | 0 | 21.53 | $471.72 | $1,203.82 | $413.98 | 20 |
| H731 | SFM-w03-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | SFM | AV | Z03 | 0 | 0 | 45.50 | $471.72 | $1,160.47 | $382.09 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | OTR | AV | Z03 | 0 | 0 | 21.53 | $471.72 | $1,203.82 | $413.98 | 20 |
| H731 | DMO-w04-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | DMO | AV | Z04 | 0 | 0 | 37.32 | $476.72 | $1,323.36 | $525.16 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | MFM | AV | Z04 | 0 | 0 | 17.13 | $454.74 | $1,160.47 | $399.08 | 20 |
| H731 | SFM-w04-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | SFM | AV | Z04 | 0 | 0 | 36.20 | $454.74 | $1,304.27 | $504.88 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | OTR | AV | Z04 | 0 | 0 | 17.13 | $454.74 | $1,160.47 | $399.08 | 20 |
| H731 | DMO-w05-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | DMO | AV | Z05 | 0 | 0 | 50.65 | $476.66 | $1,323.19 | $525.09 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | MFM | AV | Z05 | 0 | 0 | 24.23 | $511.09 | $1,304.27 | $448.53 | 20 |
| H731 | SFM-w05-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | SFM | AV | Z05 | 0 | 0 | 51.22 | $511.09 | $1,526.97 | $612.37 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | OTR | AV | Z05 | 0 | 0 | 24.23 | $511.09 | $1,304.27 | $448.53 | 20 |
| H731 | DMO-w11-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | DMO | AV | Z11 | 0 | 0 | 58.13 | $476.78 | $1,323.54 | $525.23 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | MFM | AV | Z11 | 0 | 0 | 20.39 | $598.35 | $1,526.97 | $525.11 | 20 |
| H731 | SFM-w11-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | SFM | AV | Z11 | 0 | 0 | 43.10 | $598.35 | $1,432.57 | $455.66 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | OTR | AV | Z11 | 0 | 0 | 20.39 | $598.35 | $1,526.97 | $525.11 | 20 |
| H731 | DMO-w12-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | DMO | AV | Z12 | 0 | 0 | 40.45 | $477.09 | $1,324.40 | $525.57 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | MFM | AV | Z12 | 0 | 0 | 19.55 | $561.36 | $1,432.57 | $492.65 | 20 |
| H731 | SFM-w12-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | SFM | AV | Z12 | 0 | 0 | 41.33 | $561.36 | $1,454.26 | $514.34 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | OTR | AV | Z12 | 0 | 0 | 19.55 | $561.36 | $1,432.57 | $492.65 | 20 |
| H731 | DMO-w13-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | DMO | AV | Z13 | 0 | 0 | 49.68 | $476.53 | $1,322.83 | $524.95 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | MFM | AV | Z13 | 0 | 0 | 19.27 | $569.86 | $1,454.26 | $500.11 | 20 |
| H731 | SFM-w13-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | SFM | AV | Z13 | 0 | 0 | 40.73 | $569.86 | $1,314.60 | $360.45 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | OTR | AV | Z13 | 0 | 0 | 19.27 | $569.86 | $1,454.26 | $500.11 | 20 |
| H731 | DMO-w16-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | DMO | AV | Z16 | 0 | 0 | 112.91 | $476.32 | $1,322.26 | $524.72 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | MFM | AV | Z16 | 0 | 0 | 42.17 | $515.13 | $1,314.60 | $452.08 | 20 |
| H731 | SFM-w16-vPGx-hAC-tWt-bCA-eMS-mRG-HV-EffFurn-94AFUE | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | SFM | AV | Z16 | 0 | 0 | 89.14 | $515.13 | $1,290.27 | $427.75 | 20 |
| H731 |  | 94% AFUE FURNACE (WITHOUT BUILT-IN VSM) | OTR | AV | Z16 | 0 | 0 | 42.17 | $515.13 | $1,314.60 | $452.08 | 20 |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | OTR | AV | OTR | 0 | 0 | 0.00 | $0.00 | $0.00 | $0.00 |  |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | DMO | AV | Z11 | 0.04 | 318.4 | 58.13 | $1,936.78 | $3,123.54 | $865.23 | 15 |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | MFM | AV | Z11 | 0.04 | 318.4 | 20.39 | $2,058.35 | $3,326.97 | $865.11 | 15 |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | SFM | AV | Z11 | 0.04 | 318.4 | 43.10 | $2,058.35 | $3,326.97 | $865.11 | 15 |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | OTR | AV | Z11 | 0.04 | 318.4 | 20.39 | $2,058.35 | $3,326.97 | $865.11 | 15 |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | DMO | AV | Z12 | 0.04 | 289.2 | 40.45 | $1,937.09 | $3,124.40 | $865.57 | 15 |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | MFM | AV | Z12 | 0.04 | 289.2 | 19.55 | $2,021.36 | $3,232.57 | $832.65 | 15 |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | SFM | AV | Z12 | 0.04 | 289.2 | 41.33 | $2,021.36 | $3,232.57 | $832.65 | 15 |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | OTR | AV | Z12 | 0.04 | 289.2 | 19.55 | $2,021.36 | $3,232.57 | $832.65 | 15 |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | DMO | AV | Z13 | 0.04 | 285.2 | 49.68 | $1,936.53 | $3,122.83 | $864.95 | 15 |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | MFM | AV | Z13 | 0.04 | 285.2 | 19.27 | $2,029.86 | $3,254.26 | $840.11 | 15 |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | SFM | AV | Z13 | 0.04 | 285.2 | 40.73 | $2,029.86 | $3,254.26 | $840.11 | 15 |
| H732 |  | 94% AFUE FURNACE (WITH BUILT-IN VSM) | OTR | AV | Z13 | 0.04 | 285.2 | 19.27 | $2,029.86 | $3,254.26 | $840.11 | 15 |

# Work Paper Approvals

| Grant Brohard Manager, Technical Product Support | Date |
| --- | --- |
| Dave Canny Manager, Mass Market | Date |

# Document Revision History

Revision # 		Date 		         Description		         Author (Company)

| Revision 0 | 04/11/08 | PGECOHVC123 R 0 -- 94 AFUE Furnace Residential -- Original work paper | John Shen (KEMA Services, Inc.) |
| --- | --- | --- | --- |
| Revision 1 | 06/11/09 | 94 AFUE Furnace Res PGECOHVC123 R1.doc | Christopher Li (PG&E) |
|  |  | therm impact values were derived from the 2008 DEER by taking the weighted average for buildings with and without central air conditioner (CAC). Based on RASS data, 39% of buildings with CAC and 61% without CAC. Add “OTR” Building type and “OTR” Climate zone on the at-a-glance measure table to reflect zero savings. Add “OTR” Building type on the at-a-glance measure table to reflect minimum savings. Modify NTGR from 0.80 to 0.60, ratio is the default value for HVAC measures. Modify EUL from 18 years to 20 years, EUL is based on 2008 DEER. Modify base case cost, measure equipment cost, and IMC based on 2008 DEER by taking the weighted average based on RASS data, see section 1.2 for details. 2008 DEER does not have savings value for Multi-family buildings, an assumption was made by taking the scaling factor of 47.31% from using the 2005 DEER data, for more details, see section 2.3. |
| Revision 2 | 12/01/09 | 94 AFUE Furnace Res PGECOHVC123 R2.doc | Christopher Li (PG&E) |
|  |  | 1. Add kW and kWh savings for equipments with variable speed motor (VSM), only for climate zones 11, 12, and 13. Savings where derived from PG&E work paper for VSM air handler, PGECOHVC107 R1. 2. IMC for furnace with VSM includes cost for both VSM and furnace equipments. 3. NTG of 0.6 was derived from the 2008 DEER NTG spreadsheet. 4. Updated EUL for furnace with VSM to 15 years. 5. Incorporate new measure codes for 94 AFUE furnace |
| Revision 2 | 3/16/2010 | 94 AFUE Furnace Res PGECOHVC123 R2.doc | Christopher Li (PG&E) |
|  |  | 1. Updated At-A-Glance Measure List with “OTR” building type based on using the Validation Tool. 2. Updated kW and kWh based on updated Temperature BIN simulation analysis. |

# Table of Contents

At-A-Glance Summary	i

Work Paper Approvals	vii

Document Revision History	viii

Table of Contents	ix

List of Tables	x

Section 1. General Measure & Baseline Data	1

1.1	Measure Description & Background	1

1.2 DEER Differences Analysis	2

1.3	Codes & Standards Requirements Analysis	3

1.4 EM&V, Market Potential, and Other Studies	4

1.5 Base Cases for Savings Estimates: Existing & Above Code	4

1.6 Base Cases & Measure Effective Useful Lives	4

1.7 Net-to-Gross Ratios for Different Program Strategies	5

Section 2. Calculation Methods	5

2.1 Electric Energy Savings Estimation Methodologies	5

2.2. Demand Reduction Estimation Methodologies	6

2.3. Gas Energy Savings Estimation Methodologies	6

Section 3. Load Shapes	12

3.1 Base Case Load Shapes	12

3.2 Measure Load Shapes	12

Section 4. Base Case & Measure Costs	12

4.1 Base Case(s) Costs	13

4.2 Measure Costs	13

4.3 Incremental & Full Measure Costs	14

Index	16

References	17

# List of Tables

Table 1: Electric UEC and Appliance Saturation Summaries by Utility………………………….3

Table 2: Net-to-Gross Ratios……………………………………………………………………...5

Table 3: Scaling Factor for Multi-Family building………………………………………………..8

Table 4: Measure Cost…………………………………………………………………………...13

Table 5: Incremental Measure Cost……………………………………………………………...15

# Section 1. General Measure & Baseline Data

## Measure Description & Background

This work paper documents the rational for the 94 AFUE Gas Furnace as listed in the Mass Market Residential HVAC Catalog rebate program. The Residential HVAC Catalog is part of Pacific Gas and Electric Company’s Customer Energy Efficiency Program. PG&E offers incentives to residential customers for installing qualifying equipment.

In the state of California, a large majority of heating systems use natural gas.  According to the Residential Appliance Saturation Survey (RASS) 1, 74% of all heating systems in PG&E territory run on natural gas.  Sales of central gas furnace units have also increased steadily from 413,400 units in 1999 to 578,000 units in 2005, a 40% increase.  The proportion of ENERGY STAR units sold has also increased from 9% in 2000 to 19% in 2005.  The percentages of ENERGY STAR units sold are much higher in PG&E territory at 26% in 2005.  It is important to note that the ENERGY STAR standards are currently at 90 AFUE, PG&E is promoting high efficiency units, therefore PG&E are only rebating on units with 94 AFUE or better.  Average efficiencies on units sold, however are still relatively low and have hovered between 81 and 82 AFUE in 2005.

Catalog Description

The applicant must have natural gas distributed to the installation address by PG&E for the natural gas furnace rebate and have both natural gas and electric distributed to the installation address by PG&E for the natural gas furnace and VSM rebate.  The central natural gas furnace must have a rating of 94% Annual Fuel Utilization Efficiency (AFUE) gas furnaces. For a list of qualifying products go to www.gamapower.org or

http://www.ahridirectory.org/ahridirectory/pages/home.aspx.

Program Restrictions and Guidelines

Terms and Conditions

Gas furnace units must have an efficiency level greater than or equal to 94% AFUE in any residential building.

Gas furnace units with variable speed motor are restricted to Climate Zones 11, 12, and 13.  The variable speed motor must be factory installed where it’s built into the unit.  The motor size must not exceed 10 horsepower (hp).

Market Applicability

This measure applies to all types of residential buildings, including mobile homes, single family, and multi-family buildings.

Technical Description

Furnace:

Fuel-burning furnaces provide heat by passing combustion products past a heat exchanger.  Furnaces pass inside air over the outside of the heat exchanger, transferring the heat from the fuel to the air.  Fuel-burning furnaces exhaust the products of combustion to the atmosphere through the flue passage connected to the heat exchanger. Furnaces usually have high utilization hours through the year. A gain in efficiency can therefore result in significant energy savings.

This measure is applicable to a central natural gas furnace with a rating of 94% Annual Fuel Utilization Efficiency (AFUE).  Savings stated here only apply to residential building types.

Furnace with variable speed motor:

Most existing small-scale residential heating, ventilation and air conditioning (HVAC) blowers use low cost, low efficiency, single speed motors. These motors usually range in power between 0.3hp and 2 hp. They turn on and off as required by thermostat control. This results in temperature variations, and high energy consumption of the air handler motor.

Most major HVAC manufacturers are now offering variable-speed motor air handlers. These motors have integrated electronic controls that modulate the motor and fan speed based on the cooling or heating load of the system; they run at lower speed most of the time. These motors provide much more efficient operation, and improve the quality of the air distribution; however, they come at a price premium.

This measure is designed to encourage the installation of such variable-speed motor air handlers in residential buildings. Because of the (ideally) cubic relationship between fan power and fan speed, a small reduction in fan speed can result in large energy savings. According to a DOE study that focused on variable-speed motor air handlers for residential buildings, this technology could offer 14.5 trillion Btu of savings nationwide by 2010.

## 1.2 DEER Differences Analysis

The 94% AFUE furnace measure is included in the 2008 DEER5 for residential buildings and mobile homes.  The 2008 DEER also provides savings for this measure with and without an air conditioner.  Based on the Residential Appliance Saturation Survey (RASS)1 data, 39% of customers in PG&E Territory have an air conditioner, while 61% of customers do not have an air conditioner, table 2 below describes the percentage.  Cost and savings value for this measure for multi-family will be included in future revisions of the 2008 DEER.

Table 1: Electric UEC and Appliance Saturation Summaries by Utility

Since the 2008 DEER does not include multi-family buildings, the savings were calculated by taking the scaling factor of 47.31% from using the 2005 DEER data for all PG&E climate zones.  See Section 2.3 for details.

Natural Gas furnace with variable speed motor measure does not appear in the Database for Energy Efficient Resources (DEER), therefore a BIN simulation analysis was used to estimate this savings.

## Codes & Standards Requirements Analysis

Title 20 requires all furnaces with capacities less than 225 MBtuh to have an AFUE of 78%.

Under the California Code of Regulations, Title 24, Part 6, California Energy Code, there are no mandatory requirements dictating airflow volume control devices for residential air handler systems.

## 1.4 EM&V, Market Potential, and Other Studies

There are currently no EM&V study identified that address residential furnaces or furnaces with VSM, however there is a report, “California Residential Efficiency Market Share Tracking, HVAC 2005”, prepared by Itron and completed on December 2005, that address the average annual AFUE ratings of central gas furnaces, which ranges from 81.0 to 82.6, during the study period.  This study also tracks the market share of Energy Star qualified units sold in California.

Delta Wattage Assumption (ΔW):  On the BIN analysis, the demand fan usage was assumed to be 400 watts.  This applies only for furnaces with VSM.

Net-to-Gross Assumption:  The net-to-gross assumption is taken directly from the 2008 DEER5 database as 0.605 for residential gas furnace – 90% AFUE.

In-service factor/first year installation rate:  Not an issue with this measure as it is a service and maintenance type of measure.

Hours of Operation: Residential furnaces have a wide range of effective full load hours depending on climate zone. Since DEER data are used for the calculation of energy impacts, the hours of operation are already embedded in those values.

#### Effective Useful Life:  20 years, based on 2008 DEER, for High Efficiency Furnace.  And 15 years for high efficiency furnace with variable speed motor, which is based on the DEER 2008.

## 1.5 Base Cases for Savings Estimates: Existing & Above Code

Title 20 code requirements state a minimum efficiency of 78% for furnaces.  Savings calculated in this report assume this code base case.7

The base case for furnace with VSM measure is a residential-type air handler with single speed fan motor, where the fan motor is a permanent split capacitor (PSC) single-phase motor.

## 1.6 Base Cases & Measure Effective Useful Lives

The measure effective useful life for 94 AFUE furnaces is given on the 2008 DEER as 20 years for High Efficiency Furnace.  There is no measure effective useful life for 94 AFUE furnace with variable speed motor, however there is a similar technology on the 2008 DEER for non-residential buildings for VSD Supply fan motors, which gives an EUL of 15 years.

## 1.7 Net-to-Gross Ratios for Different Program Strategies

Table 2 below summarizes all applicable Net-to-Gross ratios for programs that may be used by this measure.

Table 2:  Net-to-Gross Ratios5

| Measure Name | Program Approach | NTG |
| --- | --- | --- |
| 96% AFUE FURNACE (WITHOUT BUILT-IN VSM) | Downstream prescriptive rebate | 0.60 |
| 96% AFUE FURNACE (WITH BUILT-IN VSM) | Downstream prescriptive rebate | 0.60 |

# Section 2. Calculation Methods

## 2.1 Electric Energy Savings Estimation Methodologies

Energy savings are only applied to furnace with variable speed motor (VSM).  Energy savings calculations for gas furnace with VSM were based on a temperature-bin simulation7 method.

Temperature-bin simulations7 use HVAC performance data to calculate the efficiency of the system under the base case and measure operating conditions. The efficiency is multiplied by the HVAC load of the building, which is based on the design conditions of the building and a load profile that varies linearly with outside air temperature. The equipment demand is then multiplied by the hours of operation in each temperature bin to determine the energy consumption.

In the base and proposed cases, the air handler fan was assumed to be operating only to meet cooling and heating loads (i.e. the fan does not operate in absence of a heating or cooling load). Cooling and heating loads were based on climate data and were assumed to vary linearly with outside air temperature. Maximum cooling and heating loads were calculated based on climate-zone-specific design heating and cooling temperatures, obtained from the ASHRAE climatic design information. Therefore, in the base case, the fan runtime was equal to the load (as % of total capacity) on the heating or cooling coils; in the proposed case, the speed of the variable speed motor air handler was equal to the load on the heating or cooling coil (as % of total capacity).

A fan with a VSM behaves similarly to a fan motor with a variable frequency drive, and we used a VFD-specific relationship between fan speed and fan energy to calculate energy consumption in the proposed case. The following relationship between speed and energy consumption was used:

Where,

Power is the power consumption of than (in % of nominal power)

A, B and C are constants: A=0.21976, B=-0.8748, C=1.65259, determined from the CEC Guidebook9.

Speed is the fan speed (in % of nominal speed)

Additionally, the VSM was assumed to have a 10% higher efficiency than a standard Permanent Split Capacitor single-phase motor, based on a DOE document on variable speed motors.

We assumed an air handler motor power of 0.5 hp, and a supply air flowrate of 500 cfm, which is a standard size for air handlers where the VSM technology is applicable. To confirm our assumptions, we compared the total energy usage from our simulation for ventilation and cooling with data from the 2004 California Statewide Residential Appliance Saturation Study (RASS). The RASS reports average energy consumptions for air conditioning end-use ranging between 700 kWh/yr for town homes and 1,400 kWh/yr for single family dwellings, across all California climate zones. Air conditioning as defined by RASS is comprised of cooling and ventilation. Our simulation shows an average electric consumption of 1,180 kWh/yr for cooling and ventilation, matching the RASS data average point.

## 2.2. Demand Reduction Estimation Methodologies

Demand reduction for gas furnace with VSM was calculated based on the improved efficiency of the variable speed motor vs standard motors. Please note that since there is no Variable Frequency Drive for this application, there are no efficiency losses through a VFD device, in contrary to VFD applications. The assumptions stated in Section 2.1 above were used. The following formula was used to calculate the reduction in peak wattage:

A Power Factor of 0.80 was assumed. The base case and measure efficiencies were respectively 72% (based on the NEMA efficiency tables) and 79% (assuming a 10% efficiency increase4).

A peak hour load share of 1.0 was assumed for this measure.

Sample Calculation to determine the demand savings for furnace with variable speed motor (VSM).

## 2.3. Gas Energy Savings Estimation Methodologies

Gas savings for gas furnace with and without VSM were derived from the 2008 DEER5.  Gas savings depend on climate zone, building vintage and dwelling type.  Impact values from the 2008 DEER were determined by using the DOE2 modeling software.  2008 DEER provides impact values for buildings with and without air conditioners throughout PG&E territory.  To calculate the weighted average for buildings with and without air conditioners, the RASS1 data was used.  It was found that 39% of residential buildings in PG&E territory have an central air conditioner, while there is an assumption that 61% does not have central air conditioner, see table 2 of this report for details.

The following formula was used:

Where,

Savings (Therms/household) = Weighted average savings for this measure

DEER Impact w/AC = 2008 DEER values for building with air conditioner

DEER Impact wo/AC = 2008 DEER values for building without air conditioner

0.39 = RASS data for buildings with air conditioner in PG&E territory

0.61 =  RASS data for buildings without air conditioner in PG&E territory

Example calculation:  High efficiency furnace with a 94% AFUE, single family building located in climate zone 01.

Based on 2008 DEER, the impact value for this measure is 51.241 therms/household w/AC and 46.6891 therms/household wo/AC.

= (19.984) + (28.4803)

= 48.46 therms/household

Multi-family units are not currently listed in the 2008 DEER, but are planned to be added in the future.  To determine energy savings for those units, the savings for single family were scaled using the 2005 DEER database to compare total HVAC annual energy use between single-family, multi-family units.  The annual energy savings for single family units was then scaled based on direct ratios of total annual energy usage per the calculations below:

- From 2005 DEER, annual AC energy uses was taken for single family and multi-family units, and averaged across each vintage type.  This determined an assumed baseline energy use for each building type.

- The scaling factor for multi-family units was determined as a direct ratio:

Scaling Factor (%)= (MF AC baseline energy use) ÷ (SF AC baseline energy use)

Table 3, illustrates an example calculation of the scaling factor for PG&E territory.

Table 3: Scaling Factor for Multi-Family building.

| RunID | MeasureID | DeerMeasures.Name | NumOfCommonUnit | Base usage (kBtuh/household) |
| --- | --- | --- | --- | --- |
| RMFm0103RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 14.9002 | 8307.189304 |
| RMFm0105RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 14.9002 | 8285.032707 |
| RMFm0175RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 20.0983 | 34483.25626 |
| RMFm0185RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 23.4862 | 20168.09315 |
| RMFm0196RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 14.7502 | 7989.873586 |
| RMFm0203RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 15.9704 | 8100.889578 |
| RMFm0205RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 15.9704 | 8079.680886 |
| RMFm0275RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 28.4024 | 27202.76783 |
| RMFm0285RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 31.7028 | 15896.03754 |
| RMFm0296RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 19.7794 | 6860.900257 |
| RMFm0303RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 18.5703 | 6213.64095 |
| RMFm0305RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 18.5703 | 6199.063265 |
| RMFm0375RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 25.7783 | 29876.79192 |
| RMFm0385RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 29.341 | 16534.70978 |
| RMFm0396RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 18.3906 | 5958.536009 |
| RMFm0403RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 18.0018 | 6510.15295 |
| RMFm0405RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 18.0018 | 6494.815417 |
| RMFm0475RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 24.8335 | 28704.29765 |
| RMFm0485RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 28.3657 | 16093.79048 |
| RMFm0496RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 17.7852 | 6257.864902 |
| RMFm0503RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 19.602 | 5480.974026 |
| RMFm0505RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 19.602 | 5468.232726 |
| RMFm0575RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 27.6571 | 29947.93759 |
| RMFm0585RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 31.0303 | 15606.25496 |
| RMFm0596RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 19.3803 | 5250.006988 |
| RMFm1103RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 18.5644 | 8541.833164 |
| RMFm1105RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 18.5644 | 8519.685834 |
| RMFm1175RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 35.3978 | 29729.76267 |
| RMFm1185RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 34.2475 | 15476.27401 |
| RMFm1196RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 20.8228 | 7612.898971 |
| RMFm1203RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 17.5349 | 7921.233261 |
| RMFm1205RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 17.5349 | 7900.4018 |
| RMFm1275RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 33.337 | 27803.52472 |
| RMFm1285RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 32.5079 | 14085.28298 |
| RMFm1296RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 19.6985 | 6936.550996 |
| RMFm1303RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 17.6327 | 8504.815456 |
| RMFm1305RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 17.6327 | 8482.104539 |
| RMFm1375RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 33.4515 | 30743.0993 |
| RMFm1385RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 32.6115 | 15172.66343 |
| RMFm1396RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 19.7411 | 7354.842922 |
| RMFm1603RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 18.5313 | 17359.30646 |
| RMFm1605RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 18.5313 | 17320.79842 |
| RMFm1675RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 25.9901 | 52582.39062 |
| RMFm1685RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 29.341 | 34937.79575 |
| RMFm1696RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 18.3516 | 16916.41312 |
|  |  |  | Average Base usage: | 15108.27709 |
| RSFm0103RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 43.6502 | 34377.32611 |
| RSFm0105RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 43.6502 | 34284.61309 |
| RSFm0175RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 40.1768 | 70721.61397 |
| RSFm0185RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 32 | 37499.2 |
| RSFm0196RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 41.9312 | 33044.04988 |
| RSFm0203RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 41.2924 | 25726.19751 |
| RSFm0205RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 41.2924 | 25660.46001 |
| RSFm0275RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 69.476 | 54415.96538 |
| RSFm0285RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 51.5989 | 26145.98821 |
| RSFm0296RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 68.5313 | 25184.84156 |
| RSFm0303RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 60.4211 | 17538.55354 |
| RSFm0305RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 60.4211 | 17512.81415 |
| RSFm0375RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 56.2191 | 42762.77732 |
| RSFm0385RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 42.5951 | 18644.94015 |
| RSFm0396RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 58.1698 | 16863.076 |
| RSFm0403RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 59.1753 | 17081.83797 |
| RSFm0405RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 59.1753 | 17060.06146 |
| RSFm0475RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 53.569 | 40716.9398 |
| RSFm0485RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 42.0309 | 18280.45731 |
| RSFm0496RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 56.9611 | 16422.68259 |
| RSFm0503RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 66.3584 | 16048.51361 |
| RSFm0505RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 66.3584 | 16038.02898 |
| RSFm0575RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 61.4286 | 43328.60158 |
| RSFm0585RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 47.1287 | 16731.48969 |
| RSFm0596RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 63.75 | 15448.155 |
| RSFm1103RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 49.8466 | 24649.39293 |
| RSFm1105RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 49.8466 | 24597.65216 |
| RSFm1175RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 72.0756 | 48715.75389 |
| RSFm1185RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 68.9878 | 30413.89252 |
| RSFm1196RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 59.0698 | 22414.15375 |
| RSFm1203RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 46.1848 | 23602.00308 |
| RSFm1205RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 46.1848 | 23547.64357 |
| RSFm1275RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 67.0175 | 46011.06568 |
| RSFm1285RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 64.3019 | 28218.2458 |
| RSFm1296RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 55.0677 | 21011.41134 |
| RSFm1303RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 47.7696 | 17454.05645 |
| RSFm1305RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 47.7696 | 17417.13055 |
| RSFm1375RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 67.6105 | 35893.06224 |
| RSFm1385RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 66.0466 | 20964.18154 |
| RSFm1396RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 56.7598 | 15391.10089 |
| RSFm1603RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 67.5294 | 58206.08845 |
| RSFm1605RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 67.5294 | 58130.8607 |
| RSFm1675RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 65.7438 | 106035.5453 |
| RSFm1685RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 48.946 | 60841.83584 |
| RSFm1696RFC94 | D03-412 | Condensing 94 AFUE (1.06 HIR) Furnace | 64.8817 | 56052.40362 |
|  |  |  | Average Base Usage | 31935.70367 |
|  |  |  | Scaling Factor: | 47.31% |

Scaling Factor: 15,108.28/31,935.70 = 47.31%

- The scaling factor is multiplied by the 2008 DEER savings value for the measure:

MF Therm Savings = (Scaling Factor) * (SF Therm Savings)

Example Calculation: For climate zone Z01, 94% AFUE furnace.

SF Therm Savings = 48.46 therms/household/yr

MF Therm Savings = 0.4731 x 48.46 kWh/household/yr = 22.93 therms/household/yr

# Section 3. Load Shapes

Load Shapes are an important part of the life-cycle cost analysis of any energy efficiency program portfolio.  The net benefits associated with a measure are based on the amount of energy saved and the avoided cost per unit of energy saved.  For electricity, the avoided cost varies hourly over an entire year.  Thus, the net benefits calculation for a measure requires both the total annual energy savings (kWh) of the measure and the distribution of that savings over the year.  The distribution of savings over the year is represented by the measure’s load shape.  The measure’s load shape indicates what fraction of annual energy savings occurs in each time period of the year.  An hourly load shape indicates what fraction of annual savings occurs for each hour of the year.  A Time-of-Use (TOU) load shape indicates what fraction occurs within five or six broad time-of-use periods, typically defined by a specific utility rate tariff.  Formally, a load shape is a set of fractions summing to unity, one fraction for each hour or for each TOU period.  Multiplying the measure load shape with the hourly avoided cost stream determines the average avoided cost per kWh for use in the life cycle cost analysis that determines a measure’s Total Resource Cost (TRC) benefit.

## 3.1 Base Case Load Shapes

The base case load shape would be expected to follow a typical residential space heating end use load shape.

## 3.2 Measure Load Shapes

For purposes of the net benefits estimates in the E3 calculator, what is required is the load shape that ideally represents the difference between the base equipment and the installed energy efficiency measure.  This difference load profile is what is called the Measure Load Shape and would be the preferred load shape for use in the net benefits calculations.

The measure load shape for this measure is determined by the E3 calculator based on the applicable residential market sector and the space heating end-use.

# Section 4. Base Case & Measure Costs

The 2005 DEER Measure Cost Data Users Guide, version 2.01, defines the following terms:

- Retrofit (RET) – replacing a working technology prior to failure.

- Replace on Burnout (ROB) – replacing a technology at the end of its useful life.

Gas furnaces are suitable for RET and ROB.

## 4.1 Base Case(s) Costs

Base case cost for 94 AFUE furnace was derived from DEER 2008, the cost for this measure is $8.66 per mBtuh, which was converted to a per furnace basis using the per number common units in mBtuh furnace size, the base case cost ranges from $344.69 to $598.35 depending on the size of the furnace as well as using the RASS data showing on table 1 of this report.

There is no DEER data available for furnace with VSM measure. The costs estimates were based on a survey of equipment performed among two HVAC installers, looking at 5 different air handler models in total, to assess the true incremental cost of the measure to the customer. See appendix for detailed cost data.

The cost of a single speed, 3-ton air handler was averaged over the 2 manufacturers and was estimated at $1,460.

## 4.2 Measure Costs

Similarly to base case costs, DEER 20085 provides the cost of a gas furnace per mBtuh of furnace capacity.  Measure costs was converted to a per furnace basis using the per number common units in mBtuh and the RASS data showing on table 1 of this report.

Using the same method as for the base case costs for gas furnace with VSM, we estimated the cost of a variable speed motor, 3-ton air handler at an average $1,800. This is an installed cost for the whole air handler.  The total cost for a furnace installed in conjunction with the air handler with VSM is estimated up to $3,327.  The costs are summarized in the following table.

Table 4: Measure Cost

| Measure | Building Type | Climate Zone | Measure Cost | Labor Cost | Total Cost |
| --- | --- | --- | --- | --- | --- |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z01 | $647.19 | $232.45 | $879.63 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z02 | $1,025.04 | $368.16 | $1,393.19 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z03 | $885.71 | $318.11 | $1,203.82 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z04 | $853.81 | $306.66 | $1,160.47 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z05 | $959.61 | $344.66 | $1,304.27 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z11 | $1,123.46 | $403.51 | $1,526.97 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z12 | $1,054.01 | $378.56 | $1,432.57 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z13 | $1,069.96 | $384.29 | $1,454.26 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z16 | $967.21 | $347.39 | $1,314.60 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z01 | $894.77 | $321.37 | $1,216.14 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z02 | $895.56 | $321.65 | $1,217.21 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z03 | $895.20 | $321.53 | $1,216.73 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z04 | $895.08 | $321.48 | $1,216.56 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z05 | $894.97 | $321.44 | $1,216.41 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z11 | $895.21 | $321.53 | $1,216.74 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z12 | $895.79 | $321.73 | $1,217.52 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z13 | $894.73 | $321.35 | $1,216.08 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z16 | $894.34 | $321.21 | $1,215.55 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | SFM | Z11 | $3,326.97 |  | $3,326.97 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | SFM | Z12 | $3,232.57 |  | $3,232.57 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | SFM | Z13 | $3,254.26 |  | $3,254.26 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | DMO | Z11 | $3,123.54 |  | $3,123.54 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | DMO | Z12 | $3,124.40 |  | $3,124.40 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | DMO | Z13 | $3,122.83 |  | $3,122.83 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | MFM | Z11 | $3,326.97 |  | $3,326.97 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | MFM | Z12 | $3,232.57 |  | $3,232.57 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | MFM | Z13 | $3,254.26 |  | $3,254.26 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | OTR | Z11 | $3,123.54 |  | $3,123.54 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | OTR | Z12 | $3,124.40 |  | $3,124.40 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | OTR | Z13 | $3,122.83 |  | $3,122.83 |

## 4.3 Incremental & Full Measure Costs

Similarly to base case costs, DEER 2008 provides the cost of this measure per mBtuh of furnace capacity.  Incremental Measure costs was converted to a per furnace basis using the per number common units in mBtuh and the RASS data showing on table 1 of this report.

Furnace with VSM does not appear on the DEER 2008 database, however the IMC for this measure was found to be $340.  The costs are summarized in the following table.

Table 5: Incremental Measure Cost

| Measure | Building Type | Climate Zone | Incremental Cost |
| --- | --- | --- | --- |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z01 | $302.50 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z02 | $479.11 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z03 | $413.98 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z04 | $399.08 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z05 | $448.53 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z11 | $525.11 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z12 | $492.65 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z13 | $500.11 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | SFM | Z16 | $452.08 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z01 | $524.98 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z02 | $525.44 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z03 | $525.23 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z04 | $525.16 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z05 | $525.09 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z11 | $525.23 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z12 | $525.57 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z13 | $524.95 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) | DMO | Z16 | $524.72 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | SFM | Z11 | $865.11 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | SFM | Z12 | $832.65 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | SFM | Z13 | $840.11 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | DMO | Z11 | $865.23 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | DMO | Z12 | $865.57 |
| High Efficiency Furnace 94 AFUE (1.06 HIR) w/VSM | DMO | Z13 | $864.95 |

# Index

benchmarking	13

California Statewide Residential Lighting and Appliance Efficiency Saturation Study	17

DEER	13

DEER Measure Cost Data Users Guide	12

efficiency	2, 5, 6

ENERGY STAR	1

load shape	12

Load Shapes	12

NEMA	6, 17

Replace on Burnout	13

Residential Appliance Saturation Survey	1, 17

Retrofit	13

thermostat control	2

Time-of-Use	See TOU

Title 20	i, 3, 4, 17

TOU	12

Variable Frequency Drive	5

# References

# Endnotes

“California Statewide Residential Appliance Saturation Survey (RASS), ” prepared by KEMA, June 2004, page 4.  http://websafe.kemainc.com/RASSWEB/uploads/RASS-ExecSummary-FINAL.pdf

“California Residential Efficiency Market Share Tracking, HVAC 2005.” Prepared for Southern California Edison, page 5-1, by Itron, Inc.

“2005 California Statewide Residential Lighting and Appliance Efficiency Saturation Study,” prepared by RLW Analytics, Final Report.  August 23, 2005.  http://www.calresest.com/docs/2005CLASSREPORT.pdf

Variable Speed, Low Cost Motor for Use in Residential HVAC Systems – Department of Energy, September 2002 - http://www1.eere.energy.gov/inventions/pdfs/dynamotors.pdf

Itron, Inc.  “2008 Database for Energy Efficiency Resources”, Version 2008.2.05, December 16, 2008.  http://www.deeresources.com/

Itron, Inc.  “2004-2005 Database for Energy Efficiency Resources (DEER) Update Study, Final Report”, December 2005.

Temperature BIN Simulation by kW Engineering.

Title 20. Table E-4. Page 87.  “2007 Appliance Efficiency Regulations,” prepared by the California Energy Commission, 2007.

2001 ASHRAE Fundamentals Handbook – pages 27.8 and 27.9, Tables 1A – Heating and Wind Design Conditions, and 1B – Cooling and Dehumidification Design Conditions

“California Energy Commission Guide to Preparing Feasibility Studies”, February, 2000.

Energy Consumption Characteristics of Commercial Building HVAC Systems - Volume III: Energy Savings Potential, July, 2002.

Goodman Air Conditioning and Heating – Product specifications, Variable and Multiple-Speed Blowers – cooling capacity 1.5 to 5 tons

California Statewide Residential Appliance Saturation Study, June 2004, pg 10-11 http://www.energy.ca.gov/reports/400-04-009/2004-08-17_400-04-   009VOL2B.PDF

National Electrical Manufacturers Association (NEMA) Nominal Full Load Efficiencies

Variable Speed, Low Cost Motor for Use in Residential HVAC Systems –

Department of Energy, September 2002 -

http://www1.eere.energy.gov/inventions/pdfs/dynamotors.pdf